## Slide 1
CO3-AT-2
Quad Tree for Image Representation
A step-by-step simulation of recursive subdivision — compressing uniform regions to improve storage efficiency
Name: Jeevan R Register No: 192524007

## Slide 2
CONCEPT
What Is a Quad Tree?
A tree data structure in which every internal node has exactly 4 children, used to recursively divide 2D space into quadrants.
For images, each node represents a square region of the picture.
Uniform region (all pixels identical) → stored as a single LEAF node — no further division.
Non-uniform region (mixed pixels) → SPLIT into 4 smaller quadrants: NW, NE, SW, SE — and the process repeats.
Node
(uniform?)
splits into
NW
NE
SW
SE
Each child is checked the same way — recursively.
Jeevan R | Reg No: 192524007 | Data Structures
2

## Slide 3
PRINCIPLE
How the Compression Works
Recursive rule: uniform region → store as 1 leaf node; non-uniform region → split into 4 and repeat.
Large flat areas (sky, plain background, solid color blocks) collapse into a single large leaf — big storage savings.
Highly detailed or noisy areas keep splitting all the way down to individual pixels — little to no savings there.
Net result: compression ratio depends entirely on image content — the more uniform the image, the more it compresses.
Jeevan R | Reg No: 192524007 | Data Structures
3

## Slide 4
SIMULATION — STEP 0
Sample 8×8 Image — Raw Pixels
This is the original bitmap: an 8×8 grid of black / white pixels.
Stored naively, every single pixel needs its own value.
No structure, no grouping, no compression yet — this is our baseline.
Leaf — uniform region, stored as one node
Split — non-uniform, divide into 4
Raw storage: 64 individual pixel values.
Jeevan R | Reg No: 192524007 | Data Structures
4

## Slide 5
SIMULATION — STEP 1
First-Level Split (Depth 1)
The whole 8×8 image is checked first — it is NOT uniform, so it splits into 4 quadrants of size 4×4.
NW and SW turn out fully uniform → they become LEAF nodes immediately. Compressed!
NE and SE are still mixed → they must be split further.
LEAF
LEAF
SPLIT
SPLIT
Leaf — uniform region, stored as one node
Split — non-uniform, divide into 4
So far: 2 leaf nodes cover 32 pixels with just 2 stored values.
Jeevan R | Reg No: 192524007 | Data Structures
5

## Slide 6
SIMULATION — STEP 2
Second-Level Split (Depth 2)
NE (4×4) splits into four 2×2 blocks — all four are uniform → 4 new LEAF nodes.
SE (4×4) also splits into four 2×2 blocks — it's a checkerboard, so none are uniform → must split again.
LEAF
LEAF
LEAF
LEAF
STILL MIXED — SPLIT
Leaf — uniform region, stored as one node
Split — non-uniform, divide into 4
So far: 6 leaf nodes finalized (2 from Step 1 + 4 new). SE keeps going.
Jeevan R | Reg No: 192524007 | Data Structures
6

## Slide 7
SIMULATION — STEP 3 — FINAL
Third-Level Split (Depth 3)
Each 2×2 block inside SE splits into four 1×1 pixels.
None can merge back — the checkerboard means every neighboring pixel differs.
Result: 16 individual pixel-level LEAF nodes here — this region gets NO compression benefit.
LEAF
LEAF
LEAF
LEAF
Leaf — uniform region, stored as one node
Split — non-uniform, divide into 4
Final: 22 leaf nodes total represent all 64 pixels (see next slide for the full tree).
↑ 16 pixel-level leaves (no merge possible)
Jeevan R | Reg No: 192524007 | Data Structures
7

## Slide 8
STRUCTURE
Resulting Quad Tree
ROOT (8×8)
non-uniform
NW 4×4
LEAF – black
NE 4×4
non-uniform
SW 4×4
LEAF – white
SE 4×4
non-uniform
NW 2×2
LEAF white
NE 2×2
LEAF white
SW 2×2
LEAF white
SE 2×2
LEAF black
4 × (2×2)
all non-uniform
16 × (1×1)
LEAF pixels — no merge
(checkerboard, worst case)
Totals for this tree: 22 leaf nodes + 7 internal (split) nodes = 29 nodes total, representing all 64 original pixels.
Jeevan R | Reg No: 192524007 | Data Structures
8

## Slide 9
RESULT
Storage Efficiency Comparison
Representation | Elements Stored
Raw pixel array | 64 pixel values
Quad Tree — leaf nodes only | 22 leaf values
Quad Tree — full tree (leaf + internal) | 29 nodes
Reduction (leaves vs. raw pixels) | 65.6% fewer stored values
Why it isn't 100% compression
This sample deliberately includes a checkerboard region (SE) as a worst case — it splits all the way to single pixels with zero savings. Real photos have large uniform areas (sky, walls, backgrounds) that collapse into single leaves, so real-world compression ratios are typically much higher than this example.
Jeevan R | Reg No: 192524007 | Data Structures
9

## Slide 10
WHY IT MATTERS
Advantages & Applications
Advantages
Big compression gains on images with large flat / uniform regions.
Adjustable level of detail — stop subdividing earlier for lower resolution.
Efficient spatial queries — quickly locate the region containing a point.
Only stores detail where detail actually exists.
Applications
Image and texture compression
Level-of-detail rendering in computer graphics
Geographic Information Systems (GIS) — map tiling
Collision detection in games / simulations
Spatial indexing in databases
Jeevan R | Reg No: 192524007 | Data Structures
10

## Slide 11
Conclusion
Quad trees compress images by merging uniform regions into single leaf nodes, instead of storing every pixel individually.
Compression efficiency depends on image content: flat regions save enormous space; detailed or noisy regions save little to nothing.
In this simulation: 64 raw pixels → 22 leaf nodes (≈66% fewer stored values) — even with one deliberately ‘hard’ checkerboard region included.
Jeevan R | Reg No: 192524007 | Data Structures — CO2-AT-1